## Slide 1: PERRP Most Common Violations by Subpart
Calendar Year 2015

## Slide 2
Chart: PERRP Most Common Violations by Subpart CY 2015
| S | O | D | E | L | N | J | I | P | H
Subparts | 1062 | 591 | 240 | 172 | 162 | 148 | 140 | 116 | 114 | 99

## Slide 3
Chart: Subpart S Electrical
| 1910.305(g)(1)(iv) | 1910.303(b)(2) | 1910.304(g)(6)(vi) | 1910.303(b)(1)(iv) | 1910.303(g)(1)(ii)
Total violations 1062 | 131 | 81 | 71 | 68 | 66
Top five Subpart S standards
1910.305(g)(1)(iv): Flexible cords and cables were used as a substitute for the fixed wiring of a structure.
1910.303(b)(2): Listed or labeled electrical equipment was not used or installed in accordance with instructions included in the listing or labeling.
1910.304(g)(6)(vi): Exposed noncurrent-carrying metal parts of cord- and plug-connected equipment that may become energized were not grounded when operated at over 150 volts to ground.
1910.303(b)(1)(iv): Electrical equipment was not free from recognized hazards due to inadequate electrical insulation.
1910.303(g)(1)(ii): Working space required by this standard was used for storage.

## Slide 4
Chart: 
| 1910.215(b)(9) | 1910.215(a)(4) | 1910.212(a)(1) | 1910.212(a)(3)(ii) | 1910.212(b)
Total violations 591 | 88 | 64 | 56 | 54 | 53
Top five Subpart O standards
1910.215(b)(9): The distance between the abrasive wheel periphery(s) and the adjustable tongue or the end of the safety guard peripheral member at the top exceeded one-fourth inch.
1910.215(a)(4): Grinding machinery was not used with work rest(s) to support offhand grinding work.
1910.212(a)(1): One or more methods of machine guarding was not provided to protect the operator and other employees in the machine area from hazards such as those created by point of operation, ingoing nip points, rotating parts, flying chips and sparks.
1910.212(a)(3)(ii): Point(s) of operation of machinery were not guarded to prevent employee(s) from having any part of their body in the danger zone(s) during operating cycle(s): A metal shear was unguarded.
1910.212(b): Machine(s) designed for fixed location(s) were not securely anchored to prevent walking or moving.
Subpart O
Machinery & Machine Guarding

## Slide 5
Chart: 
| 1910.22(a)(1) | 1910.23(c)(1) | 1910.23(a)(9) | 1910.22(a)(3) | 1910.23(a)(8) | 1910.27(d)(3)
Total violations 240 | 82 | 33 | 17 | 16 | 10 | 10
Top six Subpart D standards
1910.22(a)(1): The place of employment was not kept clean and orderly, or in a sanitary condition.
1910.23(c)(1): Open-sided floors and/or platforms 4 feet or more above adjacent floor or ground level were not guarded.
1910.23(a)(9): The cover over a floor hole (grating) was missing, had openings greater than one inch wide, or was not securely held in place.
1910.22(a)(3): A floor, working area, or passageway was not kept free from protruding nails, splinters, holes, or loose boards.
1910.23(a)(8): A floor hole into which a person could accidentally walk was not guarded.
1910.27(d)(3): The side rail of a through or side-step fixed ladder extension did not extend 3 1/2 feet above the parapet or landing.
Subpart D
Walking-Working Surfaces

## Slide 6
Chart: 
| 1910.37(a)(4) | 1910.37(a)(3) | 1910.37(b)(5) | 1910.37(b)(2) | 1910.36(d)(1)
Total violations 172 | 101 | 21 | 12 | 11 | 9
Top five Subpart E standards
1910.37(a)(4): Safeguards designed to protect employees during an emergency (e.g., sprinkler systems, alarm systems, fire doors, exit lighting) were not in proper working order at all times.
1910.37(a)(3): Exit routes were not free and unobstructed.
1910.37(b)(5): Each doorway or passage along an exit access that could be mistaken for an exit was not marked Not an Exit or similar designation, or identified by a sign indicating its actual use.
1910.37(b)(2): Each exit was not clearly visible and marked by a sign reading Exit.
1910.36(d)(1): Employees could not open an exit route door from the inside at all times without keys, tools, or special knowledge.
Subpart E
Exit Routes &
Emergency Planning

## Slide 7
Chart: 
| 1910.157(e)(2) | 1910.157(c)(1) | 1910.157(e)(3) | 1910.159(c)(10) | 1910.157(d)(1)
Total violations 162 | 66 | 37 | 25 | 10 | 8
Top five Subpart L standards
1910.157(e)(2): Portable fire extinguishers were not visually inspected at least monthly.
1910.157(c)(1): Portable fire extinguishers were not mounted, located and identified so that they were readily accessible without subjecting the employees to injuries.
1910.157(e)(3): Portable fire extinguishers were not subjected to an annual maintenance check.
1910.159(c)(10): The minimum vertical clearance between sprinklers and material below was not 18 inches (45.7 cm).
1910.157(d)(1): Portable fire extinguishers were not provided for employee use.
Subpart L
Fire Protection

## Slide 8
Chart: 
| 1910.184(e)(1) | 1910.176(c) | 1910.184(e)(3)(i) | 1910.176(b) | 1910.184(c)(14) | 1910.184(d) | 1910.178(q)(7)
Total violations 148 | 36 | 18 | 14 | 10 | 10 | 10 | 6
Top seven Subpart N standards
1910.184(e)(1): Alloy steel sling(s) did not have permanently affixed durable identification stating size, grade, rated capacity, and reach.
1910.176(c): Storage areas were not kept free from accumulation of materials that constituted hazards from tripping, fire, explosion or pest harborage.
1910.184(e)(3)(i): A thorough periodic inspections of alloy steel chain slings were not made on a regular basis and/or were done at intervals greater than once every 12 months.
1910.176(b): Material was not stacked, blocked, interlocked or limited in height so that it was stable and secure against sliding and collapse.
1910.184(c)(14): A material handling sling was used that did not have permanently affixed and legible identification markings.
1910.184(d): Damaged or defective sling(s) were not immediately removed from service.
1910.178(q)(7): Industrial trucks were not examined before being placed in service.
Subpart N
Materials Handling &
Storage

## Slide 9
Chart: 
| 1910.141(b)(2)(ii) | 1910.146(c)(1) | 1910.147(c)(1) | 1910.146(c)(4) | 1910.146(c)(2)
Total violations 140 | 28 | 19 | 17 | 10 | 6
Top five Subpart J standards
1910.141(b)(2)(ii): An anti siphoning device was not installed to prevent backflow or backsiphonage into the potable water system.
1910.146(c)(1): The employer did not evaluate the workplace to determine if any spaces were permit-required confined spaces.
1910.147(c)(1): The employer did not establish an energy control program that included procedures and employee training to prevent unexpected energizing, start up or release of stored energy during machine and equipment servicing or maintenance.
1910.146(c)(4): The employer did not develop and implement a written permit-required confined space entry program.
1910.146(c)(2): The employer did not inform exposed employees of the existence and location of and the danger posed by permit-required confined spaces.
Subpart J
General Environmental Controls

## Slide 10
Chart: 
| 1910.132(a) | 1910.132(d)(1) | 1910.132(d)(2) | 1910.134(c)(1) | 1910.133(a)(1) | 1910.134(c)(2)(i)
Total violations 116 | 42 | 23 | 9 | 7 | 5 | 5
Top six Subpart I standards
1910.132(a): Protective equipment was not maintained in a sanitary and reliable condition.
1910.132(d)(1): The employer did not assess the workplace to determine if hazards were present that required personal protective equipment.
1910.132(d)(2): The employer did not verify that the required workplace hazard assessment had been performed.
1910.134(c)(1): A written respiratory protection program was not established and implemented for required respirator use.
1910.133(a)(1): The employer did not ensure each affected employee uses appropriate eye or face protection.
1910.134(c)(2)(i): Respirator users were not provided with the information contained in Appendix D when voluntary respirator use was permissible.
Subpart I
Personal Protective Equipment

## Slide 11
Chart: 
| 1910.243(b)(2) | 1910.242(b) | 1910.242(a) | 1910.244(a)(2)(vi)(a) | 1910.244(a)(1)(ii) | 1910.243(c)(3)
Total violations 114 | 31 | 22 | 19 | 19 | 11 | 9
Top six Subpart P standards
1910.243(b)(2): Compressed air hose or hose connections were not designed for the pressure and service for which they were subjected.
1910.242(b): Compressed air used for cleaning purposes was not reduced to less than 30 psi.
1910.242(a): Hand and portable powered tools or equipment were not kept in safe condition.
1910.244(a)(2)(vi)(a): Each jack used in the workplace was not thoroughly inspected at least once every six months.
1910.244(a)(1)(ii): Rated load(s) of portable jack(s) were not legibly and permanently marked.
1910.243(c)(3): Abrasive wheels used on right angle head grinders were not provided with safety guard(s) having a maximum exposure angle of 180 degrees.
Subpart P
Hand-Held Equipment

## Slide 12
Chart: 
| 1910.101(b) | 1910.106(e)(2)(ii) | 1910.106(d)(3)(ii) | 1910.125(e)(1)(i) | 1910.106(b)(2)(vi) | 1910.106(e)(6)(i) | 1910.106(g)(3)(iii) | 1910.106(g)(3)(iv) | 1910.106(g)(8) | 1910.125(f)(2)(ii) | 1910.125(f)(3)(iii)
Total violations 99 | 18 | 16 | 5 | 5 | 4 | 4 | 4 | 4 | 3 | 3 | 3
Subpart H
Hazardous Materials

## Slide 13: Most common Hazardous Materials Standards
1910.101(b): The storage and utilization of all compressed gases in cylinders, portable tanks, rail tank cars, or motor vehicle cargo tanks were not in accordance with Compressed Gas Association Pamphlet P-1.
1910.106(e)(2)(ii): Flammable or combustible liquid was not stored in a tank or closed container.

## Slide 14: Most common Hazardous Materials Standards
1910.106(d)(3)(ii)(a): Metal cabinets constructed in the following manner shall be deemed to be in compliance. The bottom, top, door, and sides of cabinet shall be at least No. 18 gage sheet iron and double walled with 1 1/2 - inch air space. Joints shall be riveted, welded or made tight by some equally effective means. The door shall be provided with a three-point lock, and the door sill shall be raised at least 2 inches above the bottom of the cabinet.
1910.125(e)(1)(i): All electrical wiring and equipment in each vapor area and any adjacent area did not conform to the applicable hazardous (classified)-area requirements of subpart S of this part (except as specifically permitted in paragraph (g) of section 1901.126).

## Slide 15: Most common Hazardous Materials Standards
1910.106(b)(2)(vi)(b): Vent pipe(s) from above ground tank(s) of Class I flammable liquids adjacent to building or public ways were less than 12 feet above adjacent ground level.
1910.106(e)(6)(i): Adequate precautions were not taken to prevent the ignition of flammable vapors.

## Slide 16: Most common Hazardous Materials Standards
1910.106(g)(3)(iii): Clearly identified and easily accessible switches or circuit breakers were not provided at a location remote from dispensing devices at an automotive service station to shut off the power to all dispensing devices in the event of an emergency.
1910.106(g)(3)(iv)(d): A Class I flammable liquid dispensing unit was not mounted on a concrete island or protected against collision damage by suitable means.

## Slide 17: Most common Hazardous Materials Standards
1910.106(g)(8): Conspicuous and legible sign prohibiting smoking not posted within sight of customer service area.
1910.125(f)(2)(ii): Vapor area(s) were not provided with an automatic fire-extinguishing system that conformed to the requirements of subpart L of this part.
1910.125(f)(3)(iii): A cover that could be closed by an approved automatic device for the automatic fire-extinguishing system was not kept closed when the dip tank was not in use.